## Slide 1: Winnetka Road to Willow Road
Happ Road Corridor Study
Village of Northfield
Steering Committee Meeting #3
February 23, 2017

## Slide 2: Meeting Agenda
Updated Project Goals Statement
Further Developed Improvement Alternatives
  Locations to be Discussed
    North Section Alternatives (Downtown)
      Standard Intersection vs. Roundabout
    Middle Section Alternatives (Happ Road Park Area)
      Standard Ped Crossing vs. Raised Refuge
    South Section Alternatives (Winnetka Intersection)
      Four-Way Stop vs. Traffic Signal
  Items to be Discussed for Each Section
    Crash Data
    Crash Analysis
    Existing Conditions Analysis
    Traffic Data and Analysis
    Refined Improvement Alternatives
Next Steps

## Slide 3: Happ Road Updated Goal Statement
Improve the Happ Road Corridor by:
Improving safety for all users
Simplifying vehicular movements at intersections
Minimizing vehicular points of conflict
Increasing awareness of pedestrians
Enhancing bicycle accommodations within the corridor, and
Creating a central place, supportive of local businesses and community gathering and walkable access.

## Slide 4: North Section (Downtown)
Happ Road Phase I Study
Village of Northfield

## Slide 5
Accident Location Map

## Slide 6
Accident Analysis
Orchard Lane Intersection:
Angle 8
Turning 5
Rear-end 2
Sideswipe 2
TOTAL: 17
Rear-end and Sideswipe Crashes tend to be less severe (i.e., fender-benders). The accident data indicates that congestion is not a major factor at this intersection.
Angle and Turning Crashes tend to result in more severe injuries. High rate of incidence indicates confusion with turn movements and the need to better delineate turning movements.

## Slide 7
Orchard Lane Intersection
Existing Traffic
2016
Projected Traffic
2040

## Slide 8
Mt. Pleasant Street Intersection
Existing Traffic
2016
Projected Traffic
2040

## Slide 9
Traffic Analysis
Level-of-Service (LOS) – Unsignalized Intersections
(stopped movements and unstopped left turns)
Ave. Delay (seconds) LOS
< 10 A
10-15 B
15-25 C
25-35 D
35-50 E
> 50 F

## Slide 10: Existing Conditions
Orchard Lane
2040 Traffic Analysis
AM LOS - C (EB) / B (WB)
PM LOS - F (EB) / D (WB)
Orchard Lane
2016 Traffic Analysis
AM LOS - B (EB) / B (WB)
PM LOS - D (EB) / C (WB)
Mt. Pleasant Street
2016 Traffic Analysis
AM LOS - B (EB) / B (WB)
PM LOS - C (EB) / B (WB)
Mt. Pleasant Street
2016 Traffic Analysis
AM LOS - C (EB) / B (WB)
PM LOS - C (EB) / C (WB)
Orchard Lane
Walnut Street
Mt. Pleasant

## Slide 11: Happ Road – Orchard Lane Intersection Alternative – Standard Intersection
LOS
Orchard Lane
2016 Traffic Analysis
AM LOS - B (EB) / B (WB)
PM LOS - C (EB) / C (WB)
Orchard Lane
2040 Traffic Analysis
AM LOS - C (EB) / B (WB)
PM LOS - E (EB) / D (WB)
Mt. Pleasant Street
2016 Traffic Analysis
AM LOS - B (EB) / B (WB)
PM LOS - C (EB) / B (WB)
Mt. Pleasant Street
2040 Traffic Analysis
AM LOS - C (EB) / B (WB)
PM LOS - C (EB) / C (WB)
Orchard Lane
Mt. Pleasant
Walnut Street
Notes: Beginning with Initial Round 1 Activities
Part 1: Identify issues and concerns
Part 2: Defining goals and objectives

## Slide 12: Happ Road – Orchard Lane Intersection Standard Intersection vs. Roundabout
vs.
Notes: Beginning with Initial Round 1 Activities
Part 1: Identify issues and concerns
Part 2: Defining goals and objectives

## Slide 13: Roundabouts – Reduced Vehicular Conflict Points
Standard Intersection =
32 Conflict Points
Roundabout =
8 Conflict Points

## Slide 14: Roundabouts Increased Pedestrian Safety
Separates Pedestrians from the Circular Movements
Shorter Crossing Distances

## Slide 15: Roundabouts and Emergency Service

## Slide 16: Roundabout Actual Safety Data
Below is the data from the Lake County Division of Transportation for the first 3 roundabouts that they built:
Number of Crashes at Roundabout Locations |  | 
Location | 2007-2010 (4 yrs) | 2012-2014 (3 yrs)
Hunt Club & Millburn | 24 | 10
Hunt Club & Wadsworth | 11 | 8
Riverwoods & Everett | 19 | 6
Hunt Club & Millburn and Hunt Club & Wadsworth were 3-way stop controlled and Riverwoods & Everett was 4-way stop controlled prior to the roundabout installation. In all cases, the severity of the crashes has lessened with the roundabouts in place.

## Slide 17: Happ Road – Orchard Lane Intersection Alternative – Roundabout (Synchro)
Notes: Beginning with Initial Round 1 Activities
Part 1: Identify issues and concerns
Part 2: Defining goals and objectives

## Slide 18: Happ Road – Orchard Lane Intersection Alternative – Roundabout #1 – 4 Leg
2016 Traffic Analysis
AM LOS - A (EB) / A (WB)
PM LOS - A (EB) / A (WB)
2040 Traffic Analysis
AM LOS - A (EB) / A (WB)
PM LOS - B (EB) / A (WB)
Walnut Street
Orchard Lane
Mt. Pleasant
Notes: Beginning with Initial Round 1 Activities
Part 1: Identify issues and concerns
Part 2: Defining goals and objectives

## Slide 19: Happ Road – Orchard Lane Intersection Alternative – Roundabout #2 – 5 Leg
2016 Traffic Analysis
AM LOS - A (EB) / A (WB)
PM LOS - A (EB) / A (WB)
2040 Traffic Analysis
AM LOS - A (EB) / A (WB)
PM LOS - B (EB) / A (WB)
Walnut Street
Orchard Lane
Mt. Pleasant
Notes: Beginning with Initial Round 1 Activities
Part 1: Identify issues and concerns
Part 2: Defining goals and objectives

## Slide 20: Happ Road – Orchard Lane Intersection Alternative – Roundabout #3 – 5 Leg Oval
2016 Traffic Analysis
AM LOS - A (EB) / A (WB)
PM LOS - A (EB) / A (WB)
2040 Traffic Analysis
AM LOS - A (EB) / A (WB)
PM LOS - B (EB) / A (WB)
Walnut Street
Orchard Lane
Mt. Pleasant
Notes: Beginning with Initial Round 1 Activities
Part 1: Identify issues and concerns
Part 2: Defining goals and objectives

## Slide 21: Summary of Alternatives
Alternatives | Pros | Cons
Standard Intersection | Meets driver expectations | Poor LOS in 2040
 | Maintains current traffic turning movements | Pedestrians have to cross at least 2 lanes of traffic at a time
 | Maintains uninterrupted traffic flow on Happ Road | 
 | Small footprint | 
Roundabout | Improved LOS | Drivers not accustomed
 | Reduced vehicle conflict points | Requires drivers on Happ to slow down through the roundabout
 | Reduced crash severity (per Insurance Institute for Highway Safety – 40% decrease in all accidents and 90% decrease in fatal accidents) | Requires a larger footprint
 | Increased pedestrian safety | No emergency vehicle priority
 | Reduce emissions and improved fuel economy by reducing idling | Restricts/Eliminates private driveway located on west side of Happ Road (South of Orchard)
 | Allows for Aesthetic enhancements | 

## Slide 22: Middle Section (Happ Road Park Area)
Happ Road Phase I Study
Village of Northfield

## Slide 23
Accident Location Map

## Slide 24
Accident Analysis
Middle (Happ Road) Section:
Fixed Object 4
Turning 2
Rear-end 2
TOTAL: 8
Fixed Object Crashes reveal the need for consideration of improved edge of pavement treatments (curb & gutter, fix shoulder drop-offs).
Turning and Rear-End Crashes indicate the need to better control speeds (traffic calming) in the two-lane section to allow for adequate stopping sight distance around the curve.

## Slide 25: Existing Conditions
Mt. Pleasant Street

## Slide 26: Existing Conditions – Park Area
Holder Lane
Colonial Lane

## Slide 27: Happ Road – South of Downtown
Mt. Pleasant Street

## Slide 28: Happ Road Park Mid-Block Pedestrian Crossing Alternatives
Without Refuge Island
Notes: Beginning with Initial Round 1 Activities
Part 1: Identify issues and concerns
Part 2: Defining goals and objectives

## Slide 29: Happ Road Park Mid-Block Pedestrian Crossing Alternatives
With Refuge Island
Notes: Beginning with Initial Round 1 Activities
Part 1: Identify issues and concerns
Part 2: Defining goals and objectives

## Slide 30: South Section (Winnetka Intersection)
Happ Road Phase I Study
Village of Northfield

## Slide 31
Accident Location Map

## Slide 32
Accident Analysis
Winnetka Road Intersection:
Angle 13
Rear-end 10
Turning 1
Sideswipe 1
TOTAL: 25
High incidence of Angle Crashes indicates confusion or lack of sight distance for movements among adjacent intersection legs.
High incidence of Rear-End Crashes indicates stop and go congestion on some intersection legs
Low Turning and Sideswipe Crashes is expected at fully stop controlled intersections

## Slide 33
Traffic Data
Happ Road at Winnetka Road Intersection:

## Slide 34: Existing Conditions – Winnetka Road
2016 Traffic Analysis
AM LOS - C (EB) / C (WB) / B (NB) / B (SB)
PM LOS - C (EB) / C (WB) / C (NB) / B (SB)
2040 Traffic Analysis
AM LOS - C (EB) / C (WB) / C (NB) / B (SB)
PM LOS - C (EB) / D (WB) / C (NB) / A (SB)
Winnetka Road
Happ Road

## Slide 35: Happ Road – Winnetka Road Intersection Alternative – 4-way Stop (SB & NB Right Turn Lanes)
2016 Traffic Analysis
AM LOS - C (EB) / C (WB) / C (NB) / C (SB)
PM LOS - C (EB) / C (WB) / C (NB) / C (SB)
2040 Traffic Analysis
AM LOS - C (EB) / C (WB) / C (NB) / D (SB)
PM LOS - D (EB) / D (WB) / D (NB) / D (SB)
Notes: Beginning with Initial Round 1 Activities
Part 1: Identify issues and concerns
Part 2: Defining goals and objectives

## Slide 36
Signal Warrant - Right Turn Only Lanes
Manual on Uniform Traffic Control Devices (MUTCD) 2009 Edition Chapter 4C: Warrant 2, Four-Hour Vehicular Volume

## Slide 37: Happ Road – Winnetka Road Intersection Alternative – Signal (SB & NB Left Turn-only Lanes)
2016 Traffic Analysis
AM LOS - B (EB) / B (WB) / C (NB) / C (SB)
PM LOS - B (EB) / B (WB) / C (NB) / C (SB)
2040 Traffic Analysis
AM LOS - C (EB) / C (WB) / C (NB) / C (SB)
PM LOS - C (EB) / C (WB) / C (NB) / C (SB)
Notes: Beginning with Initial Round 1 Activities
Part 1: Identify issues and concerns
Part 2: Defining goals and objectives

## Slide 38
Signal Warrant – Left Turn Only Lanes
Manual on Uniform Traffic Control Devices (MUTCD) 2009 Edition Chapter 4C: Warrant 2, Four-Hour Vehicular Volume

## Slide 39: Summary of Alternatives
Alternatives | Pros | Cons
4-Way Stop Control | Maintains existing roadway alignment | Maintain driver uncertainty of who is going and if vehicles are turning
 | Utilizing existing roadway pavement | Maintains unsafe pedestrian crossing condition
Traffic Signal | Improves LOS for all legs of the intersection | Increases delays at off-peak time
 | Facilitates pedestrian crossing movements in all directions | 
 | Relocates Sidewalk to within the ROW | 

## Slide 40: Next Steps
Public Meeting
    Northfield Community Center (401 Wagner Road)
    Present Alternatives
    Solicit Public Input
Consider Public Input
Refine Alternatives
IDOT Coordination
Select a Preferred Alternative
Present at Second Public Meeting

## Slide 41: Thank you for participating!
See you next time.
If you have any questions in the interim, please contact
Stacy Sigman (ssigman@northfieldil.org)
at the Village of Northfield
Steve Lynch (slynch@patrickco.com)
at Patrick Engineering
www.HappRoadStudy.com